## Slide 1: Updated Interconnect Proposal Bob Ross, Teraspeed Labs bob@teraspeedlabs.com EPEPS 2015 IBIS Summit San Jose, CA, October 28, 2015
Draft Presented September 9, 2015 at the Interconnect Working Group

## Slide 2: Background
Simplified from earlier presentations from Randy Wolff, Walter Katz, and Interconnect Task Group chair Michael Mirmak:
  http://www.eda.org/ibis/summits/may15/wolff2.pdf
  http://www.eda.org/ibis/summits/jan15/katz.pdf
  http://www.eda.org/ibis/summits/jun14/katz1.pdf
  http://www.eda.org/ibis/summits/may14/wolff.pdf
  http://www.eda.org/ibis/summits/jan14/katz.pdf
  http://www.eda.org/ibis/summits/may13/wolff.pdf
  http://www.eda.org/ibis/summits/jan13/mirmak2.pdf
  http://www.eda.org/ibis/summits/jan13/katz.pdf
Terminology simplification
  No Model_name support
  No pre-layout distinction
  Simpler I/O buffer that uses existing IBIS syntax
Note, “I/O” here is generic for all 21 IBIS [Model] Model_types

## Slide 3: Goals
Update the Interconnect proposal Terminal section based on existing IBIS keyword
Illustrate locations for Buffer, Pad, Pin
Illustrate pin_name, signal_name, and bus_label qualifiers
Illustrate buffer terminals Buffer_I/O, Puref, Pdref, (and not shown) Pcref, Gcref, Extref
Illustrate rail locations: Buffer_rail (not shown), Pad_rail, Pin_rail
Show chart of connections rules including Aggressor

## Slide 4: Definition Example
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels = signal_names
GND bus_labels = signal_names

## Slide 5: Partial Reference Diagram [Pin, Pad, Buffer] (A3, D1, D2 Omitted)
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
IBIS buffer model

## Slide 6: Terminal Syntax
[Begin Interconnect Model]
… | Other syntax
Number_of_terminals = <number> | List follows
<term_number> <terminal_type> <qualifier> <name> <Aggressor>*
… | More lines
…
[End Interconnect Model]
______________________________________________________
<qualifier>: pin_name, signal_name from [Pin] keyword,
or bus_label from [Pin Mapping] keyword,
*Optional <Aggressor> for Buffer_I/O
Convention: “shorted” connection
electrical connection

## Slide 7: Legal Interconnections
Terminal_Type / Qualifier  | pin_name | signal_name | bus_label | Aggressor
Buffer_I/O | X |  |  | A
Puref | X |  |  | 
Pdref | X |  |  | 
Pcref | X |  |  | 
Gcref | X |  |  | 
Extref | X |  |  | 
Buffer_rail |  | Y | Y | 
Pad_I/O | X |  |  | 
Pad_rail |  | Y | Y | 
Pin_I/O | X |  |  | 
Pin_rail | Y | Y |  | 
X: I/O pin_names, Y: POWER/GND names,
A: Optional Aggressor column to assign one or more aggressor buffers

## Slide 8: Reference Example
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels = signal_names
GND bus_labels = signal_names

## Slide 9: With bus_label = signal_name
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
New optional Bus_signal_name subparameter indicates that POWER/GND signal_name pins are assumed and do not have to be listed

## Slide 10: Pin-to-Buffer Interconnect Example using pin_names
[Pin Mapping] not needed, all connections are pin-to-buffer
(Similar to [Package] model direct connection to I/O buffer)

## Slide 11: Pin-to-Buffer Interconnect Example
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)

## Slide 12: Pin-to-Pad-to-Buffer Example using pin_names
[Pin Mapping] not needed, all connections are pin-to-buffer
(Similar to [Package] model direct connection to I/O buffer)

## Slide 13: Pin-to-Pad-to-Buffer Interconnect Example
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)

## Slide 14: Power Rail Interconnect Example using signal_name
[Pin Mapping] optional if bus_labels are signal_names

## Slide 15: Pin-to-Buffer Interconnect Example using signal_name for Rails
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS

## Slide 16: Example with bus_label Groups
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels
GND bus_labels

## Slide 17: Power Rail Interconnect Example using signal_names and bus_labels

## Slide 18: Pin-to-Buffer Interconnect Example with signal_names and bus_labels
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS
VDD1 VDD2 VDD3
VSS1 VSS2 VSS3

## Slide 19: Default “shorted” Connection from [Pin Mapping]
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS
VDD1 VDD2 VDD3
VSS1 VSS2 VSS3

## Slide 20: Bus_labels used for Pad names for Package to Pad Interconnect
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)

## Slide 21: Conclusions
Revised syntax
  Makes use of existing [Pin Mapping] for bus labels and defaults, [Diff Pin], [Series Pin Mapping] for two-node models
  Supports directly all 21 IBIS [Model] Model_types
  Overrides all [Package] model syntax including [Define Package Model]
  Supports IBIS-ISS (an HSPICE subset) and Touchstone electrical models
  Supports electrical models from pin-to-buffer, pin-to-bus-to-buffer, and pin-to-bus and default short from bus to buffer
  I/O buffer 1-to-1 connection assumed, but not so for POWER and GND interconnections
Issues
  Can two or more [Begin Interconnect Model]s be used together? (E.g., a pin-to-bus simplified package model and a bus-to-buffer interconnect model)