## Slide 1: Port Mapping
Walter Katz
IBIS Interconnect
February 28, 2024

## Slide 2: Arpad’s Format
! HL_PORTMAP 1.0
! PORT 1 +(PIN U1.94, A0, S) -(GROUP:GND.U1, GND, P) NAME:A0.U1.94.GNDSIDE:Die1 SIDE:Die1
! PORT 2 +(PIN U2.94, A0, S) -(GROUP:GND.U2, GND, P) NAME:A0.U2.94.GNDSIDE:Die2 SIDE:Die2
! PORT 3 +(PIN U3.94, A0, S) -(GROUP:GND.U3, GND, P) NAME:A0.U3.94.GNDSIDE:Die3 SIDE:Die3
! PORT 6 +(PIN BGA.K2, A0, S) -(GROUP:GND.BGA, GND, P) NAME:A0.BGA.K2.GND SIDE:EMDpin
! ...
! PORT 7 +(PIN U1.95, A1, S) -(GROUP:GND.U1, GND, P) NAME:A1.U1.95.GNDSIDE:Die1 SIDE:Die1
! PORT 8 +(PIN U2.95, A1, S) -(GROUP:GND.U2, GND, P) NAME:A1.U2.95.GNDSIDE:Die2 SIDE:Die2
! PORT 9 +(PIN U3.95, A1, S) -(GROUP:GND.U3, GND, P) NAME:A1.U3.95.GNDSIDE:Die3 SIDE:Die3
! PORT 12 +(PIN BGA.J2, A1, S) -(GROUP:GND.BGA, GND, P) NAME:A1.BGA.J2.GND SIDE:EMDpin
! ...
! PORT 121 +(PIN U1.71, CLK_c, S) -(GROUP:GND.U1, GND, P) NAME:CLK_c.U1.71.GND SIDE:Die1
! PORT 126 +(PIN BGA.E2, CLK_c, S) -(GROUP:GND.BGA, GND, P) NAME:CLK_c.BGA.E2.GND SIDE:EMDpin
! PORT 127 +(PIN U1.70, CLK_t, S) -(GROUP:GND.U1, GND, P) NAME:CLK_t.U1.70.GND SIDE:Die1
! PORT 132 +(PIN BGA.D2, CLK_t, S) -(GROUP:GND.BGA, GND, P) NAME:CLK_t.BGA.D2.GND SIDE:EMDpin
! ...
! PORT 163 +(GROUP:VDD.U1, VDD, P) -(GROUP:GND.U1, GND, P) NAME:VDD.VDD.U1.GND SIDE:Die1
! PORT 164 +(GROUP:VDD.U2, VDD, P) -(GROUP:GND.U2, GND, P) NAME:VDD.VDD.U2.GND SIDE:Die2
! PORT 165 +(GROUP:VDD.U3, VDD, P) -(GROUP:GND.U3, GND, P) NAME:VDD.VDD.U3.GND SIDE:Die3
! PORT 168 +(GROUP:VDD.BGA, VDD, P) -(GROUP:GND.BGA, GND, P) NAME:VDD.VDD.BGA.GND SIDE:EMDpin
! ...
! GROUP PORT 1 NAME:GND.U1, U1.2, U1.11, U1.15, U1.23, U1.38, U1.42, U1.43, U1.47, U1.50, U1.54, U1.55, U1.59, U1.60, U1.64...
! GROUP PORT 2 NAME:GND.U2, U2.2, U2.11, U2.15, U2.23, U2.38, U2.42, U2.43, U2.47, U2.50, U2.54, U2.55, U2.59, U2.60, U2.64...
! GROUP PORT 3 NAME:GND.U3, U3.2, U3.11, U3.15, U3.23, U3.38, U3.42, U3.43, U3.47, U3.50, U3.54, U3.55, U3.59, U3.60, U3.64...
! GROUP PORT 6 NAME:GND.BGA, BGA.A5, BGA.A9, BGA.A11, BGA.A14, BGA.AA5, BGA.AA13, BGA.AC5, BGA.AC9, BGA.AC11, BGA.AC14, BGA.B2, BGA.C1, BGA.C4, BGA.C5...
! ...
! GROUP PORT 7 NAME:GND.U1, U1.2, U1.11, U1.15, U1.23, U1.38, U1.42, U1.43, U1.47, U1.50, U1.54, U1.55, U1.59, U1.60, U1.64...
! GROUP PORT 8 NAME:GND.U2, U2.2, U2.11, U2.15, U2.23, U2.38, U2.42, U2.43, U2.47, U2.50, U2.54, U2.55, U2.59, U2.60, U2.64...
! GROUP PORT 9 NAME:GND.U3, U3.2, U3.11, U3.15, U3.23, U3.38, U3.42, U3.43, U3.47, U3.50, U3.54, U3.55, U3.59, U3.60, U3.64...
! GROUP PORT 12 NAME:GND.BGA, BGA.A5, BGA.A9, BGA.A11, BGA.A14, BGA.AA5, BGA.AA13, BGA.AC5, BGA.AC9, BGA.AC11, BGA.AC14, BGA.B2, BGA.C1, BGA.C4, BGA.C5...
! ...
! GROUP PORT 163 NAME:VDD.U1, U1.4, U1.8, U1.17, U1.20, U1.33, U1.36, U1.40, U1.45, U1.49, U1.52, U1.57, U1.62, U1.65, U1.67...
! GROUP PORT 163 NAME:GND.U1, U1.2, U1.11, U1.15, U1.23, U1.38, U1.42, U1.43, U1.47, U1.50, U1.54, U1.55, U1.59, U1.60, U1.64...
! GROUP PORT 164 NAME:VDD.U2, U2.4, U2.8, U2.17, U2.20, U2.33, U2.36, U2.40, U2.45, U2.49, U2.52, U2.57, U2.62, U2.65, U2.67...
! GROUP PORT 164 NAME:GND.U2, U2.2, U2.11, U2.15, U2.23, U2.38, U2.42, U2.43, U2.47, U2.50, U2.54, U2.55, U2.59, U2.60, U2.64...
! GROUP PORT 165 NAME:VDD.U3, U3.4, U3.8, U3.17, U3.20, U3.33, U3.36, U3.40, U3.45, U3.49, U3.52, U3.57, U3.62, U3.65, U3.67...
! GROUP PORT 165 NAME:GND.U3, U3.2, U3.11, U3.15, U3.23, U3.38, U3.42, U3.43, U3.47, U3.50, U3.54, U3.55, U3.59, U3.60, U3.64...
! GROUP PORT 168 NAME:VDD.BGA, BGA.A3, BGA.A4, BGA.A7, BGA.AB5, BGA.AB9, BGA.AB11, BGA.AB13, BGA.AC7, BGA.B1, BGA.B5, BGA.B9, BGA.B11, BGA.B13, BGA.C3...
! GROUP PORT 168 NAME:GND.BGA, BGA.A5, BGA.A9, BGA.A11, BGA.A14, BGA.AA5, BGA.AA13, BGA.AC5, BGA.AC9, BGA.AC11, BGA.AC14, BGA.B2, BGA.C1, BGA.C4, BGA.C5...
! ...
! CONNECT 1, 2, 3, 6; 7, 8, 9, 12; 121, 126; 127, 132;
! DIFFPORTS 127, 121; 132, 126;

## Slide 3: Walter’s Format
Port Rules
Ports
  Port Number
Type
  S Signal
  D Differential Signal
  P Power
Physical Port Name
  Physical Name
  PinDef only for Rail Nets
Logical Port Name
  Logical Name
Net
  All Ports with same Net are connected
Side
  Near/Far, can be multi drop
  Meaning of side is application dependent
Diff Port (Required if Type Differential Signal)
Port Reference (optional)
  Logical or Physical Name
  PinDef
PinDef Rules
PinDef
PinDef Name
Pin Name
Pin Name
Pin Name
…

## Slide 4: Arpad’s and Walter’s Example With No Reference Terminals
! HL_PORTMAP 1.0
! PORT 1 +(PIN U1.94, A0, S) NAME:A0.U1.94.GND SIDE:Die1
! PORT 2 +(PIN U2.94, A0, S) NAME:A0.U2.94.GND SIDE:Die2
! PORT 3 +(PIN U3.94, A0, S) NAME:A0.U3.94.GND SIDE:Die3
! PORT 6 +(PIN BGA.K2, A0, S) NAME:A0.BGA.K2.GND SIDE:EMDpin
! ...
! PORT 7 +(PIN U1.95, A1, S) NAME:A1.U1.95.GND SIDE:Die1
! PORT 8 +(PIN U2.95, A1, S) NAME:A1.U2.95.GND SIDE:Die2
! PORT 9 +(PIN U3.95, A1, S) NAME:A1.U3.95.GND SIDE:Die3
! PORT 12 +(PIN BGA.J2, A1, S) NAME:A1.BGA.J2.GND SIDE:EMDpin
! ...
! PORT 121 +(PIN U1.71, CLK_c, S) NAME:CLK_c.U1.71.GND SIDE:Die1
! PORT 126 +(PIN BGA.E2, CLK_c, S) NAME:CLK_c.BGA.E2.GND SIDE:EMDpin
! PORT 127 +(PIN U1.70, CLK_t, S) NAME:CLK_t.U1.70.GND SIDE:Die1
! PORT 132 +(PIN BGA.D2, CLK_t, S) NAME:CLK_t.BGA.D2.GND SIDE:EMDpin
! ...
! CONNECT 1, 2, 3, 6; 7, 8, 9, 12; 121, 126; 127, 132;
! DIFFPORTS 127, 121; 132, 126;
Ports | Type | Physical Port Name | Logical Port Name | Net | Side | Diff Port
1 | S | U1.94 | Mem1.A0 | A0 | Die1 | 
2 | S | U2.94 | Mem2.A0 | A0 | Die2 | 
3 | S | U3.94 | Mem3.A0 | A0 | Die3 | 
… |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 | S | BGA.K2 | Cntrl.A0 | A0 | EMDpin | 
… |  |  |  |  |  | 
7 | S | U1.95 | Mem1.A1 | A1 | Die1 | 
8 | S | U2.95 | Mem2.A1 | A1 | Die2 | 
9 | S | U3.95 | Mem3.A1 | A1 | Die3 | 
… |  |  |  |  |  | 
12 | S | BGA.J2 | Cntrl.A1 | A1 | EMDpin | 
… |  |  |  |  |  | 
121 | D | U1.71 | Mem1.CLK_c | CLK_c | Die1 | 126
126 | D | BGA.E2 | Cntrl.CLK_c | CLK_c | EMDpin | 121
127 | D | U1.70 | Mem1.CLK_p | CLK_p | Die1 | 132
132 | D | BGA.J2 | Cntrl.CLK_p | CLK_p | EMDpin | 127

## Slide 5: Schematic Symbol (for future discussion)
[Schematic Symbol]
Left_Side_Ports ! Top to Bottom
6 BGA.K2 Cntrl.A0
12 BGA.J2 Cntrl.A1
Top_Side_Ports ! Left to Right
1 U1.94 Mem1.A0
7 U1.95 Mem1.A1
Right_Side_Ports ! Top to Bottom
2 U2.94 Mem2.A0
8 U2.95 Mem2.A1
Bottom_Side_Ports ! Left to Right
3 U3.94 Mem3.A0
9 U3.95 Mem3.A1
[Schematic Symbol]
Left_Side_Ports ! Top to Bottom
6 BGA.K2 Cntrl.A0
12 BGA.J2 Cntrl.A1
Right_Side_Ports ! Top to Bottom
1 U1.94 Mem1.A0
7 U1.95 Mem1.A1
2 U2.94 Mem2.A0
8 U2.95 Mem2.A1
3 U3.94 Mem3.A0
9 U3.95 Mem3.A1