## Slide 1: Update, Restart or Fork?
Michael Mirmak
Oct. 3, 2012

## Slide 2: The Question…
Are useful package models so complex that traditional IBIS cannot be modified to support them?
  “Package” here includes on-die interconnect
  In other words, to support packages, must we…
  only add/change keywords in IBIS 5.x/6.x
  invalidate existing keywords/relationships
  … or start with a completely fresh approach?

## Slide 3: Clarifying Questions
How many models are generated today using the original package/pin/buffer intent of IBIS?
How many models use & tools support keywords outside of [Model] scope, such as [Pin Mapping] and [External Model]?
How many existing “old” IBIS files are likely to be updated with new format package data but without buffer model changes?
  Assume “old” means IBIS 4.0 and below
  Does including IBIS 4.2 and below make a difference?
  Rating the importance of existing structures &
  keywords is key to deciding next steps for IBIS

## Slide 4: What Do We Need
References to pins
References to die pads (I/O)
References to buffer power connections (may involve multiple die pad connections)
Many-to-one pad-pin connections
One-to-many pad-in connections
Simple, easy-to-understand syntax
Minimal IBIS community costs/burdens
See previous IBIS-ATM meeting proposals and lists;
Strong agreement here

## Slide 5: Pros/Cons Working List
Modify existing IBIS: Add keywords but preserving structure
  Examples: [Pin], [Model], [Component], [Pin Mapping], [Node Declarations] stand, add [Package Circuit]
Fork: Deprecate keywords and assumptions, while adding others
  Example: Remove one-to-one [Pin]/[Model] assumption, deprecate [Pin Mapping], add [Die Pads]…
“Blank Sheet of Paper”: no relationship to IBIS 5.1 assumed
  Examples: LISP-like tree hierarchy, separate model, package, component files