## Slide 1: General K-table Extraction Proposal Using SPICE Bob Ross, Teraspeed Labs bob@teraspeedlabs.com DesignCon IBIS Summit Santa Clara, California January 30, 2015 (Updated for Feb. 24, 2015 ATM Meeting)

## Slide 2: Outline
Overview
Standard IBIS Model
C_comp Variations
Generalized K-table [Kpu(t), Kpd(t)] Extraction for Standard IBIS Model
Proposed K-table Extraction Process with Extended C_comp model (and other blocks)
Concluding Comments
References from www.eda.org/ibis/summits/ on related material

## Slide 3: Overview
Standard IBIS uses a fixed value of C_comp, as seen in the standard reference model
A more detailed C_comp is needed for high-speed analysis as modelled by IBIS-ISS or by S-parameters
Interconnect BIRD proposal defines general On-die and Package blocks
Generalized method to extract and compensate for more detailed structures is proposed
Limitations remain in a more detailed model

## Slide 4
Standard IBIS Model
Package
Fixed Clamps and C_comp
Drivers

## Slide 5: C_comp Variations
Voltage (device physics)
Temperature (device physics)
Input versus I/O mode (suggest using Input model)
Frequency (C_comp might be a simplified reactance model at a measured frequency for a more complex structure, e.g., C with several parallel R-C’s)
Power connections (between all power terminals)
State dependent (low-to-high versus high-to-low)
Range (corners different than [Model] corners)
A more complex C_comp still has constant values

## Slide 6: Generalized V-T Extraction Load (with L/R/C_dut)
V(t) and I(t) can be calculated from load information

## Slide 7: Direct V(t), I(t) Solution
Xuefeng Chen, Asian IBIS Summit (China), September 11, 2007: V(t), I(t) can be extracted directly for L/R/C/V_fixture from given information by applying i=C*dv(t)/dt and v=L*di(t)/dt
This can be extended to include L/R/C_dut (where L/R/C_dut replaces the L/R/C_pin values at the measured pin)
Then the Ku(t) and Kd(t) tables can be extracted using the 2-equations/2-unknowns (2EQ/2UK) method for rising waveform or falling waveform extractions

## Slide 8: Indirect Prototype Solution Next
Originally used to investigate C_comp, L/R/C_dut and general L/R/C/V_fixture cases for K-table extraction
Calculates simultaneously K-tables [Kur(t), Kdr(t) or Kuf(t), Kdf(t)] for rising waveforms or falling waveforms based on two *_fixture based loads with corresponding V-T waveforms
Note, a 2EQ/2UK solution for the equations given later involve a determinate [I(VDET) in net-list] and SPICE based calculated K-table multiplier solutions [I(VKUR), and (I(VKDR)] as a function of both the PU and PD tables
This can also be used for I(VKUF) and I(VKDF) multiplier table generation

## Slide 9: SPICE Prototype for Ku(t), Kd(t)
Load 1
Load 2
V1 Waveform
V2 Waveform
-1E7
2EQ/2UK feedback Ku, Kd solutions using waveform errors

## Slide 10: Partial SPICE Circuit Showing 2EQ/2UK K-Table Extraction
I1(t) = Ku(t)*Iu(V1(t)) + Kd(t)*Id(V1(t))
I2(t) = Ku(t)*Iu(V2(t)) + Kd(t)*Id(V2(t))
Kdr
Kur

## Slide 11: Comments
The –1E7 negative feedback block is really a 2EQ/2UK block applied to the difference between the measured waveform and calculated waveform multiplied by a large value to provide negative “gradient” feedback
This forces convergence to the correct Ku(t) and Kd(t) solution to match simultaneously both measured and calculated waveforms
Method does not always converge – 2EQ/2UK block approximation is not an exact negative “gradient”, and/or numerical issues arise
Note, this process must be done in a vendor-specific SPICE that supports tables (versus IBIS-ISS)

## Slide 12: SPICE Numerical Comments
I-V tables entered as G elements (VCCS)
V-T tables entered as PWL voltage sources
Voltage rails can be entered
SPICE does interpolation
  Higher resolution time steps for extraction than in V-T tables
  G table currents are found by interpolation
I-V and V-T tables are also automatically extrapolated from final value
SPICE allows setting convergence criteria for more detailed interpolation curve fitting (e.g. spline)
K-tables printed out for Kur(t), Kdr(t) and separately for Kuf(t), Kdf(t)

## Slide 13: Part of SPICE Encoded IBIS Prototype for Simulation
Kur, Kdr
Kuf, Kdf

## Slide 14: General Single-ended C_comp Subckt Model
Notation and details under development
C_comp_I (if needed) attaches to internal buffer
A_signal is C_comp Subckt output
A_signal to C_comp_I resistance needs to be de-embedded from I-V tables
Model can be extended for differential connections
C_comp Subckt with series component
A_signal
C_comp_I
A_puref
A_pcref
A_pdref
A_gcref

## Slide 15: Revised, Generalized Extraction Steps Based on SPICE
Get source data: For L/R/C/V_fixture combinations, find V(T), I-V tables and encode in SPICE using VCCS and V(t) PWL elements
Create SPICE blocks: C_comp, On-die, Package blocks (if used) that will be assumed in the model
Extract K-tables: Kur(t), Kdr(t) and Kuf(t), Kdf(t), and use for internal model
Generate New V-T tables at C_comp A_signal node
  Use simple R/V_fixture loads
  V-T tables using R/V_fixture at C_comp A_signal node and I-V tables become new compensated IBIS model to generate correct K-tables

## Slide 16: SPICE Extraction of V(t), I(t) Setup and C_comp A_signal Node
PC
C_comp Subckt
GC
On-die Subckt
Package Subckt
L/R/C/V Fixture
V-T
K
-
+
Vsense = 0V
V(t), I(t)
PU, PD V(t) node and I(t) are calculated using an ideal high gain (e.g., K=1e7) operational amplifier
V-T table (originally extracted at the Fixture) is now a PWL driver

## Slide 17: 2EQ/2UK SPICE Setup to Generate Ku(t), Kd(t) Tables
2EQ/2UK Module
Ku(t) Kd(t)
Load 1
Load 2

## Slide 18: Generate New V-T Waveforms at C_comp A_signal Node (if needed)
PC
C_comp Subckt
GC
R/V Fixture
PU
PD
Kpu
Kpd
V-T

## Slide 19: EDA Tool Options
Use the originally extracted [Kur(t), Kdr(t)] and [Kuf(t), Kdf(t)] tables as drivers and along with the original PU, PD, GC, PC, and C_comp subckt
Or use PU, PD, GC, PC, C_comp subckt and NEW V-T tables for simple R/V_fixture values (if changed) and let EDA tool derive NEW K-tables that include C_comp subckt, but without Package or On-die blocks (for example, the previous slide)
  EDA tool responsible for de-embedding C_comp subckt
  Model providers would issue this simplified model

## Slide 20: Ideal Test Circuit
Reference Waveforms
  1 ns ramp into 50 W loads
  5 V supply
  2 ns duration
C_comp
  0 pF
  4 pF
  4 pF parallel with 4 pF – 50 W
Pullup/Pulldown I-V tables
  50 W straight lines
1001 point extractions

## Slide 21: K-tables versus Time (s)
Chart: 

## Slide 22: K-tables versus Time (s) – With Lfix=10 nH, Cfix=4 pF Fixtures
Chart: 

## Slide 23: Worst Case Simulation Results (Full C_comp model, full Fixture)
Chart: 

## Slide 24: Observations, Future Work
Result Accuracy
  K-table extraction Insensitive to K=1e5 to K=1e9 feedback multipliers
  Requires maximum accuracy settings
  Checked waveforms within 1.2% (about 30 mV)
  Simulation waveforms have other issues
  Not to sensitive to number of extraction points
Test cases are have severe effects
  Sharp waveform derivative discontinuity
  Large C_comp model load
  Large L_fixture, C_fixture reactive loads
Still investigating pkg (on-die) additions
  Some convergence issues with series inductance
  Series resistance in C_comp model not yet checked but should be ok

## Slide 25: Conclusions
SPICE feedback based extraction method proposed
  Does not depend on internal circuit details
  Also supports On-Die and Package blocks
  Could be implemented by mathematical code in tools
EDA tools must add de-embedding of general C_comp subckt for V-T data given at the A_signal node
Note, any “series” resistance needs to be de-embedded from the I-V tables
Some IBIS Summit references related to this presentation are given next regarding 2EQ/2UK algorithms, C_comp modeling, de-embedding, and other approaches

## Slide 26: K-table Algorithm and 2EQ/2UK Extraction
  Chen, Xuefeng
    IBIS Algorithm Including Reactive Loads (September 11, 2007) - Shows how 2EQ/2UK algorithm is solved with reactive fixture loads
    Study of Solving IBIS Single VT (November 11, 2008) - Single VT case solutions evaluated
  Muranyi, Arpad
    A VHDL-AMS Buffer Model Using IBIS V3.2 Data (June 5, 23, 2003) - A VHDL-AMS implementation and testing of 2EQ/2UK method
  Ross, Bob
    Introduction & Model Processing Algorithms (October 15, 1998) - Introduction of 1-waveform, 2-waveform extraction
    Improving IBIS ECL Algorithms (December 6, 2005) - The 2EQ/2UK algorithm is adjusted using CCVS tables
    IBIS Algorithms Revisited (June 5, 23, 2003) - K-tables described and 2EQ/2UK method extraction method proposed
    IBIS Die V-T Tables from Part or Board Measurements (February 2, 2004) - Approximate de-embedding of package and board model
  Schutt-Aine, Jose, etal.
    IBIS Modeling Using Latency Insertion Method (LIM) (May 16, 2012) – LIM method for simulation and K-T table extraction improvement

## Slide 27: C_comp Models and Extraction
  Mirmak, Michael
    Issues with C_comp and Differential Multi-stage IBIS Models (April 5, 2004) – Driver Schedule double counting and complex C_comp
    Multi-Element C_comp Modeling (October 4, 2004) – Extended C_comp model and differential C_comp
    IBIS in the Frequency Domain (July 25, 2006) – Review and discussion of extended C_comp and frequency domain impedance models
  Muranyi, Arpad
    High Accuracy Behavioral Modeling for Frequency and Time Domain Simulations (June 21, 2001) – Pole-zero extraction of complex impedance
  Giacotto, Luca
    Buffer Impedance Modeling (March 8, 2002) - Pole-zero and extended C_comp extraction
    Buffer Impedance and Quality Issues (June 13, 2002) – Pole-zero extraction as a function of bias proposal

## Slide 28: Miscellaneous De-embedding
  Ross, Bob
    IBIS Die V-T Tables from Part or Board Measurements (February 2, 2004) – Approximate de-embedding of package and board model
    C_comp and Buffer Scaling Observations (February 9, 2006) – C_fixture compensation for Driver Schedule C_comp rules
    Capacitance Compensation (February 5, 2009) – De-embedding method for C_comp and C_fixture method for Driver Schedule

## Slide 29: Sampling of Other Approaches
  Zhu, Ting, etc.
    Surrogate Model-based High-speed IO Macromodel (June 5, 2012) – Continuous equation-based PVT extraction
  Comberiate, Tom, etc.
    Using X-Parameters to Generate IBIS Models (May 15, 2013) – IBIS Model generation from X-parameters
  Stievano, Igor, etc.
    Thevinin’s Theorem Revisited (May 15, 2015) – Thevenin voltage based structure and extraction
    IC Macromodels from On-the-fly Transient Responses (May 10, 2006) – Non-linear macromodeling via parametric identification of logic gates [M(pi)log]
  Dghais, Wael, etc.
    Table-Based Extraction for Modeling Driver’s Output Admittance (May 15, 2013) – Least squares I-Q model extraction and voltage dependent capacitance effects state