## Slide 1: BIRD 166 Now, and the Affect on the Keysight Proposal with AMI_Init Impulse Response Outputs
Walter Katz
SiSoft
May 9, 2017

## Slide 2: Overview
Review of the Current BIRD 166.2
Single Redriver Flows that need to be defined with and without Keysight new IR outputs.
Conclusion

## Slide 3: Repeater Link
Repeater
Rx
Tx1
Rx1
Tx2
Rx2
channel 1
channel 2
Repeater
Repeater Tx
Incoming
(upstream)
channel
outgoing
(downstream)
channel

## Slide 4: Rx2 Input Impulse Response (IR)
In order for the Rx AMI_Init function to optimize itself correctly, the Impulse Response (IR) input must contain all the upstream equalization and channel.
  Retimer IR should include
      Channel 2
      Tx2 equalization
  Redriver IR should include
      Channel 2
      Tx2 equalization
      IR output of Rx1

## Slide 5: In the Current Redriver Flow
IR input to Rx2
  Channel 2
  Tx2 equalization
The Rx1 output is included by convolving the Rx1 IR output with the Rx2 IR output.

## Slide 6: Simple Solution
The IR input to Rx2 should be the convolution of the IR output of Tx2 with the IR output of Rx1.
The IR output of Rx2 should not be convolved with the IR output of Rx1.

## Slide 7: Single Redriver Flows that need to be defined with and without Keysight new IR outputs
In 6.1
  Tx1, Rx1, Tx2, Rx2 model an either be
    Init Only
    GetWave Only
    Dual
  There are 3x3x3x3=81 possible combinations of Init Only, GetWave Only and Dual models
With Keysight new IR outputs
  Tx1, Rx1, Tx2, Rx2 model an either be
    Init Only no additional IR outputs
    Init Only with additional IR outputs
    GetWave Only
    Dual no additional IR outputs
    Dual with additional IR outputs
  There are 5x5x5x5=625 possible combinations of Init Only with and without additional IR output, GetWave Only and Dual with and without additional IR output models

## Slide 8: Conclusion
If we do not do 166.2 in IBIS 7.0, then the Redriver flows will continue to be broken for the foreseeable future.
The 81 6.1 flows are subset of the 625 flow including the additional IR outputs.
If we do an IBIS 7.0 with BIRD 166.2 and a IBIS 7.1 with the additional IR outputs.
  IBIS 7.1 must include all 625 flows which include the 81 IBIS 7.0 flows.
  The 81 IBIS 7.0 flows in IBIS 7.1 will be identical to the 81 IBIS flows in 7.0
Writing the IBIS 7.2 flows will therefore not invalidate any of the 81 IBIS 7.0, and upward compatibility will be guaranteed.