## Slide 1: IBIS Models for DDR2 Analysis Asian IBIS Summit 2005
Barry Katz, President and CTO, SiSoft

## Slide 2: DDR Overview: Theory of Operation
Data captured on both clock edges
Data (DQ) driven source synchronously with strobe (DQS)
Proper source sync operation requires two conditions:
  DQS positioned to meet data Setup/Hold requirements
  Fixed relationship between CK and DQS must be maintained
DDR1 Clock (CK) range from 100MHz to 200MHz
  DQ 200Mbs to 400Mbs
DDR2 Clock (CK) range from 200MHz to 400MHz
  DQ 400Mbs to 800Mbs
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 3: DDR Overview: Theory of Operation
DDR1: 2.5V SSTL
DDR2: 1.8V SSTL
SSTL introduces concept of AC and DC levels
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 4: DDR System Configurations
DDR1: One to four memory modules
DDR2: One or Two memory modules
Memory Modules
  Registered and Unbuffered
  4 to 18 memory device
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 5: DDR2 Enhancements Moving beyond DDR1
Technology
  FBGA Package
  Reduced Supply Voltage (1.8V)
  Optional Differential DQS
  Improved DIMM routing Topologies
  Improved Load Balancing
  On-Die Termination (ODT)
    Increases number of combinations to simulate
  Slew-Rate Derating
    Modifies Setup/Hold requirements
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 6: On-Die Termination
DQ, DM, DQS signals only
Memory controller defined
  Transfer by transfer basis
  Dependent on loading configuration
Multiple values: 50, 75,150, and “off”
Reduces PCB component count
Simplifies system implementation
Increases analysis complexity
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 7: Data Write ODT Configurations
RCVR
VSSQ
VDDQ
300
300
System Controller
Active
Module
RCVR
One Module
Populated
Active
Module
VSSQ
VDDQ
150
150
Standby
Module
Two Modules
Populated
System Controller

## Slide 8: Data Read Configurations
System Controller
Active
Module
RCVR
One Module
Populated
Active
Module
VssQ
VDDQ
150
150
Standby
Module
Two Modules
Populated
RCVR
VSSQ
VDDQ
150
150
VssQ
VDDQ
300
300
System Controller

## Slide 9: DDR2 I/O Buffer Modeling Challenges Spice vs. IBIS
SPICE models
  Accurate, allow for PVT variation, over-clockable
  Slow simulation time
IBIS models
  Can closely match SPICE models for accuracy
  Higher simulation performance
  Multiple simulator support, readily available
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 10: DDR2 I/O Buffer Modeling Challenges ODT Modeling in IBIS
Three options for ODT modeling
  6 separate I-V curves
    Normal [Pullup], [Pulldown], [POWER Clamp] and [GND Clamp] tables
    ODT I-V curves included as [Submodel] tables
    [Submodel] usage creates portability issues
  Separate receive ODT-enabled model
    Requires switching in of separate model
    Increases complexity of simulation
    Separate simulations for every case
  4 I-V curve model with ODT enabled in receive mode
    Works well, but makes IBIS [Pullup] and [Pulldown] non-monotonic
      This is OK because sum of [Pullup] and [Pulldown] with Clamp curves is monotonic
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 11: DDR2 I/O Buffer Modeling Challenges ODT Modeling in IBIS – Thevenin ODT approach
50 Ω ODT model [GND Clamp]
50 Ω ODT model [POWER Clamp]
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 12
DDR2 I/O Buffer Modeling Challenges ODT modeling in IBIS
[Pulldown] with 50 Ω ODT characteristics subtracted
[Pullup] with 50 Ω ODT characteristics subtracted

## Slide 13
DDR2 I/O Buffer Modeling Challenges ODT modeling in IBIS
[Pulldown] combined with [* Clamp] characteristics
[Pullup] combined with [* Clamp] characteristics

## Slide 14: Future Considerations for IBIS Slew-Rate De-Rating Tables
Notes: <number>
<footer>
<header>
<date/time>
Describe Plot
Bench Data of QDR care study
Describe why reuse is important
(Significance or Picture to Paper
adequate margin is achievable
even in complex source source synch environment
REUSE as much of environment as possible (data,models, environment, DVT)

## Slide 15: Thank You!