## Slide 1: Micron’s IBIS Model Quality Process Asian IBIS Summit Shanghai, China November 11, 2008
Randy Wolff
Micron Technology
rrwolff@micron.com
Notes: <number>

## Slide 2: Overview
Micron builds in quality checks into each step of the model creation process
  Spice netlist creation
  IBIS creation process
Quality Report documentation for customers
Conclusions
Notes: <number>

## Slide 3: Spice netlist creation
Multiple pre-driver stages are included - critical timing paths unmodified
Standard Parasitic Format (SPF) netlists are created for circuits with completed layouts
SPF includes two flavors
  C only – Capacitance of all layout structures included
  RC – Resistance and Capacitance included
  RC is more accurate but creates unreasonably large netlists
  C only with additional PRC elements on critical nets can approach accuracy of RC netlist but be much smaller
Notes: <number>

## Slide 4: Spice Netlist: SPF Format Effect on Vox
In this example, PRC elements were needed to properly model the effect of long, imbalanced metal lines between the pre-driver logic and pre-driver stages.
Quality : Correct Vox level

## Slide 5: Determining C_comp min/max
C_model_min = C_package + C_comp_min
C_model_max = C_package + C_comp_max
Quality : Correct C_package and C_comp

## Slide 6: Correlating I-V curves to Measurements
Must match exact Process/Voltage/Temp conditions between Spice simulation and Measurement
Process model adjustment example
  Process corners set by parameter range: -1=Slow, 0=Typical, 1=Fast
  IDSN model corners (uA/um) (for specific Vds and Vgs voltage setting)
    Slow: 359.0 Typical: 399.8 Fast: 450.9
    Silicon Measurement: 397.3, Adjusted 6.1% towards Slow (-0.061)
  IDSP model corners (uA/um)
    Slow: 173.1 Typical: 203.7 Fast: 242.1
    Silicon Measurement: 194.1 , Adjusted 31.5% towards Slow (-0.315)
Notes: <number>

## Slide 7: Correlating I-V curves to Measurements
Model = yellow, Measurement = red
Before PVT Adjustment After PVT Adjustment
Quality : I-V curves match measurements
Notes: <number>

## Slide 8: Model Quality
Model Creation Checklists
  Spice model development
    : Transistor model libraries setup and correlated to speed grades
    : Correct power supply decoupling included in netlists
    : Variable capacitance added to PAD node for proper C_comp variation
    : Clamp diode currents adjusted through bulk node resistance
    : All control signal combinations function properly
Notes: <number>

## Slide 9: Model Quality
Model Creation Checklists
  IBIS model development
    : Run IBISCHK – explain any warnings
    : Component names and Pin lists agree with the datasheet
    : Input model parameters match the datasheet
    : I/O model parameters match the datasheet
    : V-t curves time correlated and on/off time relationships valid
    : Combined Submodel curves show proper ODT voltage midpoint termination and resistance
Notes: <number>

## Slide 10: Quality Reports
IBIS Open Forum – IBIS Quality Task Group
  Released the IBIS Quality Specification, Rev 1.0, 3/31/04
  Currently working on an updated release
Micron follows the IQ Spec, but releases a detailed report with each model
  Compares model to specification data
  Compares model to measurement data
  Compares IBIS model to HSPICE model

## Slide 11: Quality Reports - Introduction

## Slide 12: Quality Reports – IQ Summary
IBIS Quality Summary included based on IQ 1.0 specification
Report will detail IQ 1.1 spec once released
IBIS model does not include full IQ Summary, but instead states:
|IQ SUMMARY Overall Quality of component and models Level 2b
|See Micron IBIS Model Quality Report for full IQ SUMMARY

## Slide 13: Quality Reports – IOH/IOL vs. Spec

## Slide 14: Quality Reports – C_comp, ODT & Slew Rates vs. Specification
ODT
C_comp
Slew Rates

## Slide 15: Quality Reports – C_comp & IOH/IOL vs. Measurement
C_comp
IOH/IOL

## Slide 16: Quality Reports – IBIS vs. HSPICE
Test load

## Slide 17: Conclusions
Model users demand quality models
IBIS Quality Committee work is essential for standardizing quality levels and methods
IBIS Quality checklists work to maintain quality standards
Quality Reports go above and beyond checklists to document thorough model checking
Demand Quality models from vendors!
  Show them examples of quality models.

## Slide 18
Notes: <number>