## Slide 1: Port Mapping Draft 28 – RefDes and EMD Issues
Michael Mirmak, Intel Corp.
April 7, 2026

## Slide 2: Globbing vs. Shorting – An Opinion
Globbing: referring to a collection (e.g., of terminals) without assuming any action related to connectivity; definitional
  For instance, defining a single reference location for multiple signals
Shorting: making a connection between all members of the collection
  Group here is also a short, because of its usage in Port Mapping
Proposal: * means globbing in all cases; it’s the location or usage of the wildcard that determines shorting or not…

## Slide 3: Issue 1: RefDes Definition
Page 8 of Port Mapping Draft 28, “Physical”:
  “For a Touchstone file which describes a printed circuit board (PCB) system, the value argument to a ‘Physical’ name should be a reference designator (also called a ‘refdes’), followed by a dot and a pin number (e.g., U7.3).“
While true for PCB usage, is this a universal rule we should enforce (i.e., for X.Y, Y is always a pin and never anything else)?
Should this definition be made applicable to the entire Port Mapping keyword?
  Reminder: EMD, IBIS Interconnect, etc. connections are only supported under “Physical”
  Reminder: <designator>.<pin_name> format is supported for EMD Type S and P

## Slide 4: Issue 2: EMD Links and Rail Names
Example 12 :
Example 13 :
Example 14 :
The Physical references in all three examples are supposed to be ”rail signal names”
How would a tool or reader know this?
What does this mean (“rail signal names” is not defined for Port Mapping)
Why only rail signals?
  A: “The asterisk character (“*”) may be used as a wildcard for Data_usage EMD to represent multiple terminals, but only in the context of ports identified as “Type P” (meaning, where rails are involved).”
Other text states the following are allowed for Type P:
  an EMD <pin_name >
  <designator>.<pin_name>
  Bus_label.<name>
  Group.<name>
  Bus_label.<designator>.<name>
  Group.<designator>.<name>
  Bus_label.*.<name>
  Group.*.<name>
Also Type S!