## Slide 1: Port Mapping Proposal for Touchstone 3.0: Resolving Reference Language and Connection Nomenclature
Michael Mirmak, Intel Corp.
March 11, 2026
Prepared for the IBIS Interconnect Task Group

## Slide 2: “Probe” vs. “Physical” Language in Proposal
Probe: The Probe value identifies the location of the terminal where the Port data is captured, either through simulation or lab measurement. Specifically, this is a set of coordinates identifying the terminal location. The value argument to the “Probe” name shall be an X:Y:Z string, with each value, representing a coordinate, separated from other coordinates by the colon (“:”) character. Whitespace separating the coordinate values and the colon character is permitted. X and Y values shall be numeric (floating point) values and are assumed to define distances. Because PCB system descriptions in Touchstone files may involve either a physical distance (e.g., the top of a connector on a PCB) Z may be a numeric (floating point) value to describe a distance, or to describe a layer within a PCB stackup, the Z value may be a non-negative integer or a string without whitespace. The coordinate origin is arbitrary and not stated in the Touchstone file, but all coordinates used in a single Touchstone file port map shall use the same origin. Note that Probe values may refer to a measurement fixture or system not described in the Touchstone file data. This fixture or system may be distinct from any terminal information in Net and/or Physical used for connectivity to other components.
Probe coordinate values have no meaning for the purposes of connectivity, unlike Net and Physical values.
{Change: make reference optional for Probe; if present, the reference should be specified through a location only, instead of A_gnd or a string name}
Physical: The value for the name “Physical” is a string that describes the physical location of a terminal (and optionally its reference) for use in connection to other devices, circuit elements, etc. This is at minimum a pin name for a component (such as “B1” on a connector). The string should clearly indicate where, for instance, the terminal on the described circuit element is to be connected to other terminals in a circuit simulator netlist. The value following the Physical name is not intended to identify the function of the terminal (the “Logical” name is intended for use in associating terminals with functional labels). A Physical name-value pair refers to an individual terminal of the associated Port.
For a Touchstone file which describes a printed circuit board (PCB) system, the value argument to a “Physical” name should be a reference designator (also called a “refdes”), followed by a dot and a pin number (e.g., U7.3). Because there is no explicit identification (i.e., no Data_usage or other reserve term) for PCB systems that can be automatically read, the usage of reference designator syntax is a recommendation to the model maker. …
The rules defined below can be followed to automatically connect the circuit described by the Touchstone network data using Physical name-value pairs to external IBIS [Interconnect Model]s, IBIS [EMD Model]s, IBIS [C Comp Model]s, IBIS AMI Ts4file analog circuits, and IBIS-defined PI models. The value provided in the various <name>, <pin_name>, and <designator> fields shown below shall match the value used in the IBIS or EMD file referencing this Touchstone file. For this reason, if Data_usage is present for a given Port Map, a Physical name-value pair shall be present for all Ports in that Port Map.
Physical value identifiers and Net value identifiers (described above) are the primary mechanisms by which connectivity information between the ports of a Touchstone data set used as a model and its surroundings (e.g., other Touchstone files, SPICE component descriptions, IBIS packages, etc.) may be provided. Nevertheless, Touchstone files do not name the IBIS-related files, SPICE netlists, etc. that describe the components to which the ports of the Touchstone data set may be connected. Instead, the connectivity is defined in the external calling file (e.g., the SPICE netlist, the [Interconnect Model] keyword of an IBIS file, the [EMD Model] keyword of an EMD file, the Ts4file parameter in an AMI file, etc.) that instantiates the Touchstone file with its appropriate syntax. The information contained in the Touchstone port mapping section facilitates automated generation of such connectivity syntax in the calling files, and/or checking the consistency between the Touchstone file and calling files.

## Slide 3: A_gnd and Reference Assumption Language
Port Subparameter:
  (p.5) “Note that a Port always denotes a pair of terminals; the reference terminal may be explicitly identified using the syntax defined below or, if not explicitly identified, is assumed to be A_gnd.”
  (p. 6): “The “-“ symbol is used to associate these name-value pairs with the reference terminal of the port; the “-“ symbol may also be used with a Physical Group of terminals.”
  “If the “–“ symbol is not present for a port, the reference terminal for that port is connected to A_gnd {Change: re-phrase to ensure A_gnd assumption refers only to Physical, Net}. Note that A_gnd may not appear for the Logical, Net, Physical, or Probe name-value pairs associated with the non-reference terminal of a Port.”

## Slide 4: A_gnd and Reference Assumption Language (2)
(p. 10) “Name-value pairs for Logical, Net, Physical, or Probe preceded with a “-“ character define how the reference terminal for that function of the port is connected, or the reference terminal used for measurement for that function. The value in these reference terminal name-value pairs may be different for each port or may be the same for some ports (in any combination) or may be the same for all ports. A_gnd may be used as the reference terminal of some or all ports. Using A_gnd in a name-value pair identified with “-“ is equivalent to omitting that name-value pair since A_gnd is the assumed (or default) reference connection. This notation helps model makers document how the probes or ports were set up in the lab measurements or extraction software simulations. Note that the use of A_gnd for Logical name-value references does not have meaning in terms of connectivity, measurement, or defining a return path; it is simply a label. Similarly, for Probe, the use of A_gnd does not have meaning in terms of connectivity or defining a return path; the “A_gnd” string for Probe, if present, simply names a common reference used for measurement of the provided data without specifying a precise physical location.“

## Slide 5: Current Connectivity “Caution” Language
(p. 10) “How referencing is handled when the Touchstone data is used in simulation is entirely up to the user of the data or the EDA simulation software. Care must be taken to ensure that Touchstone data used as models and other circuit blocks (if present) are connected without compromising the loop behavior of the overall circuit being simulated.”

## Slide 6: Nomenclature Checking
Wildcards for EMD; Syntax Comparisons for IBIS Interconnect

## Slide 7: EMD Wildcard Definitions
“Wildcard” as a term is only used twice in IBIS 8.0… and not for EMD
(p. 408) For Terminal_type_qualifier, for signal_name:
  “*.<signal_name> shall represent all of the [Designator Pin List] <signal_name> entries at all [Designator Pin List] interfaces shorted together.”
(p. 409) For Terminal_type_qualifier, for bus_label:
  “*.<bus_label> shall represent all of the [Designator Pin List] <bus_label> entries at all [Designator Pin List] interfaces shorted together.”

## Slide 8: EMD Wildcard Definitions (2)
(p. 410) For designator interfaces, involving rails:
  “For all designator interfaces, terminals with the same signal_name may be reduced to a single terminal for modeling purposes with the syntax:
  <Terminal_number> Pin_rail signal_name <*.signal_name>
  For all designator interfaces, terminals with the same bus_label may be reduced to a single terminal for modeling purposes with the syntax:
  <Terminal_number> Pin_rail bus_label <*.bus_label>
  This syntax excludes rail terminals at the [EMD Pin List] interface. There may exist electrical connections between all of the *.<name> terminals. The connections are not necessarily physical shorts on any one interface or between any of the interfaces. “

## Slide 9: IBIS Interconnect vs. Port Mapping IBIS_Interconnect Syntax
IBIS Interconnect
  pin: Pin_I/O, Pin_Rail, A_gnd
  die pad: Pad_I/O, Pad_Rail, A_gnd
  buffer: Buffer_I/O, Buffer_Rail, Pullup_ref, Pulldown_ref, Power_clamp_ref, Gnd_clamp_ref, Ext_ref, A_gnd
Port Mapping
  Physical Name Formats
    pin.<pin_name> (Type S or Type P)
    pad.<pin_name> (Type S or Type P)
    buf.<pin_name> (Type S only)
  Buffer Rail Connection Formats
    Pullup_ref.<pin_name>
    Pulldown_ref.<pin_name>
    Power_clamp_ref.<pin_name>
    Gnd_clamp_ref.<pin_name >
    Pullup_ref.Bus_label:<name>
    Pulldown_ref.Bus_label:<name>
    Power_clamp_ref.Bus_label:<name>
    Gnd_clamp_ref.Bus_label:<name>
    Pullup_ref.Group:<name>
    Pulldown_ref.Group:<name>
    Power_clamp_ref.Group:<name>
    Gnd_clamp_ref.Group:<name>
    Ext_ref
    A_gnd