## Slide 1: BIRD 166 Now, and the Affect on the Keysight Proposal with AMI_Init Impulse Response Outputs
Walter Katz
SiSoft
May 9, 2017

## Slide 2: Repeater Link
Repeater
Rx
Tx1
Rx1
Tx2
Rx2
channel 1
channel 2
Repeater
Repeater Tx
Incoming
(upstream)
channel
outgoing
(downstream)
channel

## Slide 3: Tx1 and Rx1 are Dual Models, Tx2 and Rx2 are both Init-only Slide 3 Problem_in_BIRD166_Flow.pptx
Now rewrite Rx1 GetWave output as VRx1GW(t) = d(t)h1 + dV. Here dV represents
Nonlinearity in Rx1, e.g. limiting mode redriver and compression
Redriver internal noise
Xtlk signals that enter Rx1
Tx2
Rx2
Channel 2
Tx1
Rx1
Channel 1
Note that . If upstream channel has X dB loss, then
redriver nonlinearity, noise and xtlk are amplified by X dB when they reach Rx2 DFE

## Slide 4: In Slide 4 Problem_in_BIRD166_Flow.pptx, Fangyi Contemplates
The time domain waveform at the output of Rx2 is determined by convolving the output of Rx1 AMI_GetWave with some IR that represents the IR of Tx2, Channel 2, and Rx2, and that there is no valid way of determining this combined IR correctly and also include as input to the Rx2 the IR of the full channel including the section between and including Tx1 and Rx1.
The current flow in IBIS 6.1 does not say to do this.

## Slide 5: The current flow in IBIS 6.1 does says:
In the Repeater Flow Section
  Step 8a. Redriver: The simulation platform uses the signal waveform at the output end of Rx1’s algorithmic model in step 7, regardless whether Rx1’s AMI_GetWave exists or not, as the stimulus of Tx2’s algorithmic model, regardless whether Tx2’s AMI_GetWave exists or not, and performs simulation on the downstream channel, which consists of Tx2, physical channel 2 and Rx2, according to the AMI flow defined in the spec for channels without Redrivers.
In the AMI flow defined in the spec for channels without Redrivers
  Step 6c. If Tx GetWave_Exists is False and Rx GetWave_Exists is False, the output of Step 4 (digital stimulus) is convolved with the output of Step 3 (output of Rx) by the EDA tool and the result is passed on to Step 8.

## Slide 6: My Interpretation of IBIS 6.1 Is
Step 8a. Redriver: The simulation platform uses the signal waveform at the output end of Rx1’s algorithmic model in step 7, regardless whether Rx1’s AMI_GetWave exists or not, as the stimulus of Tx2’s algorithmic model, regardless whether Tx2’s AMI_GetWave exists or not, and performs simulation on the downstream channel, which consists of Tx2, physical channel 2 and Rx2, according to the AMI flow defined in the Spec for Channels WithOut ReDrivers SCWORD).
If Tx2’s AMI_GetWave does not exists the output of Step 4 in SWORD (digital stimulus) is convolved with the output of Step 6 (output of Rx) by the EDA tool.

## Slide 7: This Ignores the Tx1 and Rx1 AMI GetWave
In IBIS 6.1 there is no mathematically precise way to use the time domain functionality of Tx1 and Rx1 AMI_GetWave if Tx2 and Rx2 do not have an AMI_GetWave and include all of the equalization of Tx2 and Rx2 and simultaneously include in the input to Rx2 all of the equalization between and including Tx1.
And there will not be a mathematically precise way to do this in IBIS 7.x that includes the Keysight BIRD of adding additional IR outputs to AMI_Init if the model make does not either make his Init-Only AMI Models Dual models or add the additional IR outputs so that the EDA tool can make proxy AMI_GetWave models.

## Slide 8: I Repeat
What would be the bad affects of passing BIRD 166.3 now, and then implement the Keysight BIRD with additional IR outputs of AMI_Init in IBIS 7.x