## Slide 1: [Pulldown Reference] [GND Clamp Reference] Offset in [Pulldown] [Ground Clamp]
Walter Katz
IBIS GND Editorial
March 4, 2016

## Slide 2: VDD Relative is Clear in Pullup and Power Clamp Curves
Keyword: [POWER Clamp Reference]
Required: Yes, if the [Voltage Range] keyword is not present
Description: Defines a voltage rail other than that defined by the [Voltage Range] keyword as the reference voltage for the [POWER Clamp] I-V data.
Other Notes: The I-V table of the [Pullup] and the [POWER Clamp] structures are “Vcc relative”, meaning that the voltage values are referenced to the Vcc pin. (Note that, under these keywords, all references to “Vcc” refer to the voltage rail defined by the [Voltage Range], [Pullup Reference], or [POWER Clamp Reference] keywords, as appropriate.) The voltages in the data tables are derived from the equation:
Vtable = Vcc – Voutput

## Slide 3: VDD Relative is Clear in Pullup and Power Clamp Curves
Keyword: [GND Clamp Reference]
Required: Yes, if the [Voltage Range] keyword is not present
Description: Defines a power supply rail other than 0 V as the reference voltage for the [GND Clamp] I-V data. If this keyword is not present, the voltage data points in the [GND Clamp] I-V table are referenced to 0 V.
Would be nice to add
Other Notes: The I-V table of the [GND Clamp] structure is “GND relative”, meaning that the voltage values are referenced to the GND pin. (Note that, under these keywords, all references to “GND” refer to the voltage rail defined by the [GND Clamp Reference] keywords.) The voltages in the data tables are derived from the equation:
Vtable = Voutput -GND

## Slide 4: What is the Meaning of Vtable = Vcc – Voutput Vtable = Voutput –GND
Device Under Test (DUT, In Vitro)
  Vtable = [Power Clamp Reference] – Voutput
  Vtable = Voutput –[GND Clamp Reference]
Device In Action (DIA, In Vivo)
  Vtable = (Power Clamp Reference Pin) – Voutput
  Vtable = Voutput –(GND Clamp Reference Pin)

## Slide 5: What is the Meaning of VinL and VinH?
Device Under Test (DUT, In Vitro)
  Guaranteed Low
    Voutput < VinL
  Guaranteed High
    Voutput > VinH
Device In Action (DIA, In Vivo)
  Guaranteed Low
    Voutput – ((GND Clamp Reference Pin)-[GND Clamp Reference]) < VinL
  Guaranteed High
    Voutput – ((GND Clamp Reference Pin)-[GND Clamp Reference]) > VinH
Example
  If
    [GND Clamp Reference]=0.0V and [Power Clamp Reference] =5.0V
    VinL=1.0V, VinH=4.0V
    (GND Clamp Reference Pin]=10.0V and [Power Clamp Reference Pin] =20.0V
  Then
    Guaranteed Low
      Voutput < 11.0
    Guaranteed High
      Voutput > 14.0