## Slide 1: BIRD181.1 Terminology Issues Bob Ross bob@teraspeedlabs.com IBIS Editorial Task Group March 24, 2017

## Slide 2: Issues and Choices
Delay BIRD181.X until V7.0
Finalize BIRD181.X only
Fix other I-V tables, text, and node references
  [ISSO *] keyword and Figures 7-10
  [Series MOSFET] Figure 14 and Equations
  [Composite Current Figure 16 and Text
  Section 9 Notes on Derivation Method Tables, Text, Figures
Fix all areas related to references
  Timing test load Figures 1, 2 ground symbol
  Terminator Reference Figure 11
  Figure 15 ground symbol
  Figure 30 ground symbol
  Figure 31 voltage references or ground symbol reference

## Slide 3: BIRD181.X Interaction
Reference terminals or nodes consistent with Interconnect BIRD189
*_ref are terminal or node locations
AMI Touchstone BIRD158.X Ground lines or ground triangle in figures relate to drawing with ground
Much of other IBIS V6.1 content

## Slide 4: References
In BIRD189, Locations are at Pin, Pad, Buffer interfaces
Vcc is used in Version 6.1– be careful
*_ref are terminal or node locations
For defining [Pullup], [Pulldown], [POWER Clamp], [GND Clamp] I-V table Vtable entries, the associated *_ref nodes refer to the keywords of the corresponding [* Reference] typ/min/max voltages
For simulation, these reference voltages can be modulated for each corner

## Slide 5: BIRD181.1 I-V Table (orig., newer)
Other Notes: The I-V table of the [Pullup] and the [POWER Clamp] structures are “Vcc relative”, meaning that the voltage values are referenced to the Vcc pin. (Note that, under these keywords, all references to “Vcc” refer to the voltage rail defined by the [Voltage Range], [Pullup Reference], or [POWER Clamp Reference] keywords, as appropriate.) The voltages in the data tables are derived from the equation:
Vtable = Vcc – Voutput
Other Notes: The I-V table of the [Pullup] and the [POWER Clamp] structures are “Pullup_ref relative”, meaning that the voltage values are referenced to the Pullup_ref pin. (Note that, under these keywords, all references to “Pullup_ref” refer to the voltage rail defined by the [Voltage Range], [Pullup Reference], or [POWER Clamp Reference] keywords, as appropriate.) The voltages in the Voltage column of the data tables are derived from the equation:
Vtable = V(Pullup_ref, Buffer_I/O)

## Slide 6: BIRD181.2 I-V Table (orig., better?)
Other Notes: The I-V table of the [Pullup] and the [POWER Clamp] structures are “Vcc relative”, meaning that the voltage values are referenced to the Vcc pin. (Note that, under these keywords, all references to “Vcc” refer to the voltage rail defined by the [Voltage Range], [Pullup Reference], or [POWER Clamp Reference] keywords, as appropriate.) The voltages in the data tables are derived from the equation:
Vtable = Vcc – Voutput
Other Notes: The I-V table of the [Pullup] structure is “Pullup_ref relative”, meaning that the voltage values are referenced to the Pullup_ref pin. (Note that, under this keyword, all references to “Pullup_ref” refer to the voltage rail defined by the [Voltage Range] or [Pullup Reference] keywords, as appropriate.) The voltages in the Voltage column of the data tables are derived from the equation:
Vtable = V(Pullup_ref, Buffer_I/O)

## Slide 7: [ISSO PU] Figure and Text
The effective current table for the Isso_pu current is extracted by the following process. The buffer is set to “logic one”. A Vtable voltage source is inserted between the [Pullup Reference] node and the buffer shown below. This Vtable voltage is swept from -Vcc (typical) to +Vcc (typical) and is relative to the [Pullup Reference] typ/min/max values for the corresponding columns. The output is connected to the GND (typical???) value as shown in Figure 8.
[Pullup Reference] 
Buffer rail node for extraction 
[Pulldown Reference]

## Slide 8: [ISSO PU] Proposed Changes
The effective current table for the Isso_pu current is extracted by the following process. The buffer is set to “logic one”. A Vtable voltage source is inserted between the Pullup_ref node and the buffer terminal associated with the Pullup_ref as shown below. This Vtable voltage is swept from –Vcc (typical) to + Vcc (typical) and is relative to the Pullup typ/min/max values for the corresponding columns. The output is connected to the Pulldown_ref (typical???) value as shown in Figure 8.
Pullup_ref 
Buffer Pullup_ref node 
Pulldown_ref
Replace Vcc with V(Pullup_ref, Pulldown_ref) above and in figure

## Slide 9: [ISSO PU], Also Add
As with BIRD181.X, Add definitions of the *_ref terminals:
(Note that, under this keyword, all references to “Pullup_ref” refer to the voltage rail defined by the [Voltage Range] or [Pullup Reference] keywords, as appropriate.)
*_ref can be the typ/min/max values for the terminal
Or *_ref can be the buffer terminal at the buffer for K-table simulation for a specific corner
Nomenclature issue applies other keywords and figures

## Slide 10: Conclusion, Questions
Be precise about [* Reference] and *_ref nodes for Vtable in I-V extractions and for simulation models
*_ref nodes should be used for K-table simulation equations (not shown)
Did we mean “typical” connections for [ISSO PU], [ISSO PD] even although the figure shows typ/min/max?
Text and figure changes considered together
Also, Buffer_I/O versus Buf_I/O in BIRD189 – needs to be resolved

## Slide 11: I-V Table Ranges

## Slide 12: I-V Table Ranges
Table | Low Voltage | High Voltage
[Pulldown] | -Vtyp(Pullup_ref, Pulldown_ref) | 2*Vtyp(Pullup_ref, Pulldown_ref)
[Pullup] | -Vtyp(Pullup_ref, Pulldown_ref) | 2*Vtyp(Pullup_ref, Pulldown_ref)
[Pulldown] (ECL) | 0.0 V | 2.2 V
[Pullup] (ECL) | 0.0 V | 2.2 V
[GND Clamp] | -Vtyp(Power_clamp_ref, Gnd_clamp_ref) | Vtyp(Power_clamp_ref, Gnd_clamp_ref)
[POWER Clamp] | Vtyp(Power_clamp_ref, Gnd_clamp_ref | 2*Vtyp(Power_clamp_ref, Gnd_clamp_ref)
[Series Current] | -Vtyp(Power_clamp_ref, Gnd_clamp_ref) | Vtyp(Power_clamp_ref, Gnd_clamp_ref)
[Series MOSFET] | 0.0 V | Vtyp(Power_clamp_ref, Gnd_clamp_ref)
[ISSO PD] | -Vtyp(Pullup_ref, Pulldown_ref) | Vtyp(Pullup_ref, Pulldown_ref)
[ISSO_PU] | -Vtyp(Pullup_ref, Pulldown_ref) | Vtyp(Pullup_ref, Pulldown_ref)

## Slide 13: I-V Table Extraction Ranges
Table | Low Voltage | High Voltage
[Pulldown] | -V(Pulldown_ref, 0.0) – Vtyp(Pullup_ref Pulldown_ref) | V(Pulldown_ref, 0.0) + 2*Vtyp(Pullup_ref), Pulldown_ref)
[Pullup] | -V(Pullup_ref, 0.0) – 2*Vtyp(Pullup_ref Pulldown_ref) | V(Pullup_ref, 0.0) + Vtyp(Pulldown_ref), Pulldown_ref)
[Pulldown] (ECL) | V(Pulldown_ref -2.2) | V(Pulldown_ref, 0.0)
[Pullup] (ECL) | V(Pullup_ref -2.2) | V(Pullup_ref, 0.0)
[GND Clamp] | -V(Gnd_clamp_ref, –Vtyp((Power_clamp_ref, Gnd_clamp_ref) | V(Gnd_clamp_ref, 0.0) +Vtyp(Power_clamp_ref, Gnd_clamp_ref)
[POWER Clamp] | V(Power_clamp_ref, 0.0) | V(Power_clamp_ref, 0.0) + Vtyp((Power_clamp_ref, Gnd_clamp_ref)