## Slide 1: Simulation [Model]s in IBIS Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
Future Editorial Meeting
April 22, 2016

## Slide 2: Rail Terminals
IBIS modeling format can be partitioned:
  Models: [Model], [* Series], etc.
  Pinout: [Component], [Pin], [Diff Pin], [Series Pin Mapping], [Pin Mapping], etc.
  Package information: [Package], *_pin, [Define Package Model], etc.
  Specification and information: header information, Model_type, Vinh, Vinl, [Model Spec], etc.
[Model] extraction or [Model] usage means the rail terminal have different meanings
  This can impact how we name the rail terminals

## Slide 3: [Model] Flow
[Model] (“DUT”) content
(Mathematical) simulation [Model]
Simulation circuit with [Model]s
Vdd
Vss
I/Os
[Model]
Simulation Model
Simulation Circuit can include pinout, package, models and external rails

## Slide 4: [Model] Summary
[Voltage Range], [* Reference]
[Pullup], [Pulldown], [POWER Clamp], [GND Clamp]
[Ramp], [Rising Waveform], [Falling Waveform], [Initial Delay] with/without [Composite Current]
[ISSO PU], ISSO PD]
C_comp, C_comp_*, [C Comp Corner]
… etc.
[Add Submodel], [Submodel]
Information and Specifications:
Model_type, Vinh, Vinl, Vref, Vmeas, etc.
[Model Spec], [Receiver Thresholds]
Plus post processing and possible [* Reference] shifting:
Smooth the data, make monotonic
Extrapolate or truncate the tables
Time shift data, etc.
[Model]
All content based of fixed references in the [Model] or “ground” (no pins are involved)

## Slide 5: [Model] from “DUT”
Standard: I-V, [Ramp], V-T tables, C_comp or split C_comp
[ISSO PU], ISSO PD] for “gate” modulation (for multipliers of K-table multipliers)
[Composite Current] for SSO effects due to actual power current modulation effects including pre-driver and crowbar currents
Add RLC “tweak” as Series model to rail terminals
ALL EXTRACTIONS on SPICE simulation model without package and assume FIXED internal [* Reference] voltages with respect to “ground”

## Slide 6: Figure 16 - Extraction Setup Showing [Composite Current]
C_comp effects included in DUT

## Slide 7: Basic IBIS I/O [Model]
Rails fixed for extraction, can be varied for simulation

## Slide 8: Figure 17 – “DUT” Internal Currents & [Composite Current]
[Composite Current] WF1, WF2, …
Derived current
“DUT”
Add [* Series] models to rails for “tweaking”

## Slide 9: Gate Modulation Effect
Based on static extractions
[ISSO PU], [ISSO PD] tables in [Model]

## Slide 10: Figures 7, 8 for ISSO Extractions
All content based of fixed references in the [Model] (no pins are involved)

## Slide 11: Figures 9 K-table referenced for ISSO Data Collection

## Slide 12: Simulation Model Summary
Fixed clamps and other I-V tables
K-table (PU, PD) I-V table switching multipliers
Kpur(t), Kpdr(t), Kpuf(t), Kpdf(t)
Ksso_pd(Vtable_pd), Ksso_pu(Vtable_pu) K-table
scaling for gate modulation adjustment
Internal rail to rail current adjustments based on
measured [Composite Current]s plus on-die
decoupling
C_comp splitting, if needed
Add single [* Series] model between rails
for tweaking [Composite Current]s
Simulation Model
All content based of fixed references in the [Model] (no pins are involved)

## Slide 13: EDA Tool Reference [Model]s for Simulation
Four rails
C_comp to GND or split C_comp options available; with or without I-V tables
Not shown - reference models supporting all other Model_types (e.g., ECL, Open_drain, Open_source, Terminators, Differential models, etc.)

## Slide 14: Possible IBIS Simulation Model
Core K-table based simulation model
Additions for ISSO & gate modulation
Additions for split C_comp
EDA vendors may have differences
  Algorithms
  “Ground” references
  Crowbar current extraction (adjustment) for simulation

## Slide 15: K(t) Multiplier Table Simulation Model (Not Official)
Derived from fixed, constant rails ([* Reference]) and I-V and V-T tables and C_comp in the IBIS model
Same K(t) multipliers with C_comp to GND or split C_comp to any or all rails
Fixed Rail terminals from [* Reference] voltages relative to “ground”

## Slide 16: K-table IBIS I/O [Model]
Can add split C_comps

## Slide 17: Add Rail Internal Currents to Match [Composite Current]
[Composite Current] WF1, WF2, …
Derived current
“DUT”
Add [* Series] models to rails for “tweaking”
How DUT “adjustment” currents are added is not described, but some fixed effects need to be subtracted from the “measured” [Composite Current] information

## Slide 18: Figures 10 Gate Modulation K-table Dynamic Scaling Adjustments
Fixed rails for table extraction, variable rails for simulation model

## Slide 19: Simulation Circuit
Vdd
Vss
I/Os
Add package model [Package], *_pin, [Define
Package Model]
Add pinout [Pin]
Add [Pin Mapping], if needed
Add external rails (can be fixed or can fluctuate)
External rails override the [* Reference] voltages
Nodes of each model can now vary due to current from the [I-V] tables during simulation with fixed or varying external rails (due to impedance of the rail package models and DYNAMIC effects):
K-table multipliers
Ksso_* scaling
Internal crowbar current RLC adjustments and
external decoupling circuit

## Slide 20: Completing Simulation Circuit
Add package models for I/O terminal
Add package models for rails (not well defined)
Add [* Series] model (rail to rail) for composite current adjustment (N in parallel for N buffers??)
Split C_comp?
Add loads
No one approach is “correct”, EDA tools have differences
Note, other model/simulation algorithms exist (e.g., using multiple bases for models)