## Slide 1: [Pin Pad Map] Proposal (Version 2) Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
IBIS Interconnect Task Group
December 15, 2015

## Slide 2: GND Pin Only Example - Pin_rail and Pad_rail Terminals
[Pin Pad Map] keyword proposal
  Replaces [Bus Labels] and [Die Supply Pads]
  Equivalent information, without indirection confusion
  Not needed if pad_name not used
[Begin Interconnect Model] used only to define terminals
  IBIS-ISS file or Touchstone file contains the electrical interconnection model information
  While the intended interconnect topology is shown, the actual topology and coupling depends on electrical contents that connect to the terminals
Physical interconnection shown first
Nine interconnection modeling cases
  Fewer terminal cases support simplified modeling extractions

## Slide 3: Legal Pin/Pad_rail Terminals
Terminal_Type / Qualifier  | pin_name | signal_name | bus_label | pad_name | Aggressor
Buffer_I/O | X |  |  |  | A
Puref | X |  |  |  | 
Pdref | X |  |  |  | 
Pcref | X |  |  |  | 
Gcref | X |  |  |  | 
Extref | X |  |  |  | 
Buffer_rail |  | Y | Y |  | 
Pad_I/O | X |  |  |  | 
Pad_rail |  | Y | Y | Z | 
Pin_I/O | X |  |  |  | 
Pin_rail | Y | Y | Y |  | 
X: I/O pin_names, Y,Z: POWER/GND names, Z: from [Pin Pad Map]
A: Optional Aggressor column to assign one or more aggressor buffers

## Slide 4: Pad_rail to Bus_rail Connections
[Pin Pad Map] table used to illustrate Pad_rail to Bus_rail connections
(Commented Lines are assumed to be the Bus_rail connections)

## Slide 5
Pin and pad association under [Pin Pad Map] keyword with [Pin] and [Pin Mapping]

## Slide 6
pin_name and pad_name terminals for modeling physical interconnection

## Slide 7
signal_name terminals for simplified interconnect model

## Slide 8
bus_label terminals for higher resolution simplified electrical model

## Slide 9
Terminals for modeling Pin_rail signal_name and Pad_rail bus_label interconnection

## Slide 10
Remaining terminal selection options for electrical interconnect model extraction and simplification (some options may be impractical)

## Slide 11: Pad_rail to Buffer_rail Terminals
Connection terminals extended to Buffer_rail
[Pin Mapping] is needed for connecting I/O buffer supplies to Buffer_rail terminals
Direct Pad_rail to I/O buffer supply pins would use Pdref, Gcref (and possibly Puref, Pcref and Extref) terminals
Six connection possibilities, although some may be impractical
Pad_rail interface must be the same as Pin/Pad and Pad/Buffer terminal descriptions

## Slide 12: Legal Buffer/Pad_rail Terminals
Terminal_Type / Qualifier  | pin_name | signal_name | bus_label | pad_name | Aggressor
Buffer_I/O | X |  |  |  | A
Puref | X |  |  |  | 
Pdref | X |  |  |  | 
Pcref | X |  |  |  | 
Gcref | X |  |  |  | 
Extref | X |  |  |  | 
Buffer_rail |  | Y | Y |  | 
Pad_I/O | X |  |  |  | 
Pad_rail |  | Y | Y | Z | 
Pin_I/O | X |  |  |  | 
Pin_rail | Y | Y | Y |  | 
X: I/O pin_names, Y,Z: POWER/GND names, Z: from [Pin Pad Map]
A: Optional Aggressor column to assign one or more aggressor buffers

## Slide 13
Pad_rail pad_name to on-die Buffer_rail signal_name terminals
Buffer_rail qualifiers

## Slide 14
Pad_rail pad_name to on-die Buffer_rail bus_label terminals
Buffer_rail qualifiers

## Slide 15
Pad_rail signal_name to on-die Buffer_rail signal_name terminals
Buffer_rail qualifiers

## Slide 16
Pad_rail bus_label to on-die Buffer_rail bus_label terminals
Buffer_rail qualifiers

## Slide 17
Pad_rail signal_name to on-die Buffer_rail bus_label terminals
Buffer_rail qualifiers

## Slide 18
Pad_rail bus_label to on-die Buffer_rail signal_name terminals
Buffer_rail qualifiers

## Slide 19: Comments
[Pin Pad Map] keyword not needed if pad_name is not used
  Pins and pads are merged during extraction
  However, documenting them may be informative
[Pin] signal_name or [Pin Mapping] define Buffer_rail connections to Buffer_I/O supply terminals (Pdref, Gcref, Puref, Pcref, Extref) when using Buffer_rail
Bus_label_signal_pin simplifies [Pin Mapping] and makes signal_name and bus_label qualifiers redundant and identical

## Slide 20
[Pin Pad Map] and [Die Supply Pads] Comparison

## Slide 21: Trade-offs
[Pin Pad Map]
  One less column
  Less indirections since pin_name column gets signal_name from [Pin], or bus_label from [Pin Mapping] listings
  pin to pad mapping shows physical association (although some may be simplified since actual IBIS-ISS or Touchstone file describes interconnection)
  May require a few more lines for many pins to 1 pad cases
[Die Supply Pads]
  Both signal_name and bus_label columns needed and be checked for consistency with [Pin] and [Pin Mapping] entries
  Pin_names for each pad_name must be found indirectly from [Pin Mapping]
  Hard to visualize the physical package association