## Slide 1: Interconnect Modeling – Bus_Labels in Four Ways Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
IBIS Interconnect Task Group
August 23, 2017

## Slide 2: Four Ways (with Simple Example)
[Pin Mapping] (existing Version 6.1)
Default [Pin] signal_name ([Pin Mapping] extension)
  BIRD182
[Bus Label]
  BIRD189
[Die Supply Pads]
  BIRD189
Any combination of above

## Slide 3: [Pin Mapping] (V6.1 Syntax)
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS VDD | BL0, BL1
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
10 VSS NC | BL0 for VSS
11 NC VDD | BL1
12 NC BL2
13 NC BL3
14 NC BL4
bus_label for each GND and POWER pin_name

## Slide 4: [Pin Mapping] BIRD182
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS VDD | BL0, BL1
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
| 10 VSS NC | BL0 for VSS
| 11 NC VDD | BL1
12 NC BL2
13 NC BL3
14 NC BL4
bus_label = signal_name by default

## Slide 5: Add [Bus Label]
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS VDD | BL0, BL1
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
| 10 VSS NC | BL0 for VSS
| 11 NC VDD | BL1
12 NC BL2
| 13 NC BL3
14 NC BL4
[Bus Label] signal_name
|
BL3 VDD

## Slide 6: Add [Die Supply Pads]
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS VDD | BL0, BL1
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
| 10 VSS NC | BL0 for VSS
| 11 NC VDD | BL1
12 NC BL2
| 13 NC BL3
| 14 NC BL4
[Bus Label] signal_name
|
BL3 VDD
[Die Supply Pads] signal_name bus_label
|
Pad4 VDD BL4

## Slide 7: All Together
Simple example shows all four methods:
  One POWER or GND net for each bus_label
  Normally more nets would be combined
Explicit bus_label entries in [Pin Mapping] for POWER/GND pin_name lines (IBIS V6.1)
signal_name for bus_labels:
  by default (BIRD182)
  by [Bus Label] (BIRD189)
  by [Die Supply Pads] (BIRD189)
Any or all methods can be used at once
Buffer_Rail in Interconnect BIRD189 needs [Pin Mapping] for buffer rail terminals

## Slide 8: [Die Supply Pads] Default Note
[Die Supply Pads] without bus_label entry defaults to bus_label = signal_name
If [Pin Mapping] uses [Pin] signal_name = bus_label, then [Die Supply Pads] default entry is redundant
However, if signal_name is NOT a bus_label in any [Pin Mapping] column, and the [Die Supply Pads] entry defaults to signal_name, and if this default is used as a Buffer_Rail bus_label entry; there is no connection to any I/O buffer rail
The default may still may be used as a Pad_Rail bus_label or Pin_Rail bus_label terminal
This might be considered a fifth way to define and use bus_label

## Slide 9: [Die Supply Pads] Default Note
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS BL1 | BL0, BL1 (was VDD)
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
| 10 VSS NC | BL0 for VSS
11 NC BL1 | BL1 (was VDD)
12 NC BL2
| 13 NC BL3
14 NC BL4 | Explicitly defined
[Bus Label] signal_name
|
BL3 VDD
[Die Supply Pads] signal_name bus_label
|
Pad4 VDD | VDD by default
bus_label = signal_name, either redundant with BIRD182 or may be used with Pad_Rail or Pin_Rail (*)
* Buffer_Rail bus_label VDD not with any I/O here

## Slide 10: Original [Die Supply Pads]
[Pin] signal_name model_name
|
| ... IO Models
1 IO1 IO1
2 IO2 IO2
3 1O3 IO3
4 1O4 IO4
|
| ... Rails with different bus_label entries
10 VSS GND
11 VDD POWER
12 VDD POWER
13 VDD POWER
14 VDD POWER
|
[Pin Mapping] pulldown_ref pullup_ref
|
1 VSS VDD | BL0, BL1
2 VSS BL2
3 VSS BL3
4 VSS BL4
|
| ... Rails and bus_label definitions
| 10 VSS NC | BL0 for VSS
| 11 NC VDD | BL1
12 NC BL2
| 13 NC BL3
| 14 NC BL4
[Bus Label] signal_name
|
BL3 VDD
[Die Supply Pads] signal_name bus_label
|
Pad4 VDD BL4