## Slide 1: Interconnect Set Syntax Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
Interconnect Meeting
July 13, 2016

## Slide 2: Syntax Choices

## Slide 3: [Interconnect Model Set] – Names
[Interconnect Model Set Selector]
Set_1 *.ibs | or file_name.ims
Set_2 *.ibs
Set_3 *.ibs
…
[End Interconnect Model Set Selector]
[Interconnect Model Set] Set_1
IO_Pin_1
PDN_ALL
[End Interconnect Model Set]
[Interconnect Model Set] Set_2
IO_Pin_2
PDN_ALL
[End Interconnect Model Set]
[Interconnect Model Set] Set_3
IO_ALL
PDN_ALL
[End Interconnect Model Set]
[Interconnect Model] PDN_ALL
File_IBIS-ISS <file_name.iss> PDN_ALL
Number_of_terminals = 4
Buffer_Rail signal_name VSS
Buffer_Rail signal_name VDD
Pin_Rail signal_name VSS
Pin_Rail signal_name VDD
[End Interconnect Model]
[Interconnect Model] IO_Pin_1
...
[End Interconnect Model]
[Interconnect Model] IO_Pin_2
...
[End Interconnect Model]
[Interconnect Model] IO_ALL
...
[End Interconnect Model]

## Slide 4: [Interconnect Model Set] Syntax Choices
Include complete [Interconnect Model]s
  No indirection, everything included
  May need to scroll several pages to see all the content
Include [Interconnect Model]s by name
  Easily visible list of contents
  Can instantiate [Interconnect Model]s
  Does not close door to instantiation
Each [Interconnect Model Set] and called [Interconnect Model]s in same file (.ibs or .ims)