## Slide 1: Package Modeling Status
Walter Katz
IBIS Open Forum
December 6, 2013

## Slide 2: Overview
Decisions Made
What These Decisions Means
Next Decisions
Conclusions

## Slide 3: Decisions Made
Decisions Made | In .ibs | In EMD
Connectors | No | Yes
Cables | No | Yes
Broadband EBD | No | Yes
MCM | No | Yes
Interposers | No | Yes
3-D structures | No | Yes
Stacked Memory | No | Yes
Splits/Joins of Signal (I/O) in Pacxkage or Die | No | Yes
RDL as separate element | No | Yes
New list of supply (PDN) die pads | Yes | Yes
Separate package and on-die interconnect model | Yes | Yes
Package model can include on-die model | Yes | Yes
Broadband I/O Package Modeling | Yes | Yes
Package PDN | Yes | Yes
Broadband I/O On-Die Modeling | Yes | Yes
On-Die PDN | Yes | Yes
Interconnect coupling (crosstalk) between I/O and I/O | Yes | Yes
Interconnect coupling between I/O and PDN | Yes | Yes
Optical Interconnect | No | No

## Slide 4: What These Decisions Mean
For signal (I/O) pins there is a one to one correspondence between Pin Number, Die Pad, and Buffer.
There is a Few to Many or Many to Few relationship between supply (PDN) pins and supply die pads, and buffer Pullup, Pulldown, Power Clamp and Ground Clamp Reference terminals.
There MAY be a one to one correspondence between signal (I/O) Pin Numbers and Signal Names (IBIS 6.0 is not clear on this).

## Slide 5: Next Decisions
Do we support sNp directly without requiring they be wrapped in a subckt?
Port naming options
  Can we identify signal (I/O) ports using Signal_name?
  Can we identify supply (PDN) ports using Signal_name?
  Can we identify signal (I/O) ports using Model_name?
Syntax Details
  Should Parameters have Typ, Min, Max values?

## Slide 6: Conclusion
Interconnect subcircuit ports can have a naming protocol that uniquely identifies each pin, die pad and buffer terminal that can be used at each port of a package or on-die interconnect model.
The port naming protocol can be extended to classes of ports such as signal name, or model name in addition to pin number and die pad name.
Port naming protocol can be parameter tree, or shorthand naming convention.
EMD-Like and BIRD 125 are functionally similar, just syntactical details.